## Slide 1
SAEISS ADDC 2025
TECHANICAL PRESENTATION
TEAM PHOENIX AERO
TEAM ID:ADDC2025031
TEAM PHOENIX AERO

## Slide 2
Objective:
  Develop an autonomous drone for safe and secure medical supply
Key points:
  Frame and structural design
  Payload mechanism
  Automation
INTRODUCTION
TEAM PHOENIX AERO

## Slide 3
CONFIGURATION
Quad-X configuration is preferred due to its advantages:
  Reduces drag and maximizes thrust
  Uses differential thrust for yaw, pitch, and, roll
  Ensures uniform flight with high motor efficiency
TEAM PHOENIX AERO

## Slide 4
AERIAL DESIGN
TEAM PHOENIX AERO

## Slide 5
Components | Material
Propeller | ABS
Main body | PLA+
Propeller Guard | PLA+
Landing Gear | Aluminum
Arms | Carbon Fibre
MATERIAL
ABS
Carbon fibre
PLA+

## Slide 6
COMPONENTS
Brushless Motors
  Brushless motors eliminate friction from brushes.
  Reduces energy loss and improve efficiency.
  Can achieve higher RPMs allowing for faster response and greater thrust.
  High torque.
T Motor MN3110
TEAM PHOENIX AERO

## Slide 7
COMPONENTS
TEAM PHOENIX AERO
Electronic Speed Controller
  Faster response to analog and PWM protocols
  Reduced heat generation
  Handles higher current load
Emax 35A BLHeli-S firmware
TEAM PHOENIX AERO

## Slide 8
COMPONENTS
  Good balance of strength and flexibility
  Relatively light-weight
  Quieter operation
Propellers
11X4.5 Inch Propellers
TEAM PHOENIX AERO

## Slide 9
COMPONENTS
TEAM PHOENIX AERO
Pixhawk 6c
Flight Controller
  Supports various flight modes.
  Compact and light weight design
  High processing power for sensor data fusion
  Advanced power management capabilities
TEAM PHOENIX AERO

## Slide 10
COMPONENTS
Battery
  Longer flight time
  Prevents overheating during high discharge
  Higher energy density
  Lesser internal resistance
  Consistent power supply
3300 mAh Bonka
LiPo Battery
TEAM PHOENIX AERO

## Slide 11
COMPONENTS
On-board Computer
  Powerful processor
  Multiple USB ports
  Expandable memory
  Multiple memory configurations
  Compatible camera module
Raspberry pi 4b
TEAM PHOENIX AERO

## Slide 12
COMPONENTS
Global Positioning System
  RTK HERE 3+ GPS provide horizontal accuracy within centimeters.
  Support multiple GNSS constellation including GPS, GLONASS , Galileo and BeiDou for improved accuracy and reliability
RTK-GPS HERE3+
TEAM PHOENIX AERO

## Slide 13
COMPONENTS
Lidar
  Provide accurate distance measurement and obstacle detection.
  Ensure drone stability during autonomous mission.
TF-Mini-S
TEAM PHOENIX AERO

## Slide 14
TOTAL WEIGHT ESTIMATION
10
11
12
13
Telemetry
Lidar
Camera
Miscellaneous
Total
1
1
1
7
8
9
5
6
GPS
Onboard Computer
1
1
3
4
Flight Controller
1
Sr No.
Name/Component
Quantity
Weight per Q (gm)
Weight
1
2
ESC
4
15
60
60
60
51.8
52
52
51.8
5.3
24
3
24
5.3
3
100
100
1867.1
982.9
21
Battery & Power Modules
1
690
690
Propellers & Guards
4
26
104
T-Motor
4
98
392
Frame & Rods (4)
1
52
265
TEAM PHOENIX AERO
Payload & Payload Mech.
1
160
160

## Slide 15
SAFETY FEATURES
  A drone safety feature that automatically brings the drone back to its takeoff point if it loses signal or has low battery.
  Using GPS, the drone follows a safe route to land at the exact launch location, preventing fly-aways and crashes.
Return to Launch (RTL)
TEAM PHOENIX AERO

## Slide 16
SAFETY FEATURES
  A drone safety feature that automatically disables the motors after a certain period of inactivity or upon landing.
  It is especially useful in emergency situations or when the drone is idle for too long.
Auto disarm
TEAM PHOENIX AERO

## Slide 17
SAFETY FEATURES
  A propeller guard for drones is a protective frame around the propellers that prevents damage and enhances safety.
  It protects people, objects and the drone itself from accidental contact while improving flight stability.
Propeller guard
TEAM PHOENIX AERO
Propeller guard

## Slide 18
MANUFACTURING
TEAM PHOENIX AERO

## Slide 19
TESTING VIDEO
TEAM PHOENIX AERO

## Slide 20
PAYLOAD BAY DESIGN
Payload Bay Design
  Stable and lightweight cubical structure optimized for strength and efficiency, made from durable materials like craft board and foam.
  Hinged door with a controlled 90° opening to minimize impact forces on the payload.
  Dual-servo mechanism ensures secure locking and smooth operation.
  Auto-reset feature closes the door for the next use.
TEAM PHOENIX AERO

## Slide 21
DROPPING MECHANISM
Payload Loaded
Payload Unloading
Payload Unloaded
TEAM PHOENIX AERO

## Slide 22
AUTONOMOUS MISSION
Overall Autonomous mission planning on Mission Planner
  Initial Preparation – Setting up for the operation.
  Defining GPS Coordinates & Planning Route – Determining the flight path.
  Takeoff – Drone begins the mission.
  Scanning for QR Code – Searching for a target QR code.
  Three Possible Outcomes:
  QR Code Not Detected → Drone proceeds to the destination.
  Recognition at Destination → Retrieves data, hovers, and drops payload.
  Recognition Before Destination → Proceeds with retrieval and precision hovering.
  Payload Dropping – Delivering the package.
  Returning to Launch Base – Mission completion.
TEAM PHOENIX AERO

## Slide 23
QR CODE DETECTION
Take off
Scanning for QR code
Recognition of QR code at destination
Recognition of QR code before destination
QR code is not detected
Retrieval of the data in
the QR code.
Precision hovering over the QR code
Payload dropping
Arrival at destination
TEAM PHOENIX AERO

## Slide 24
INNOVATION
Unique and Protective Drone Design
  The quadcopter boasts a compact, aerodynamically shaped body that provides effective component placement.
  The design focuses on weight saving, strength and improved performance.
  Specially designed propeller guards offer maximum protection with least airflow obstruction.
Aerodynamic shape
TEAM PHOENIX AERO

## Slide 25
INNOVATION
Graphical User Interface (GUI)
  A custom-built GUI simplifies mission planning for better user experience.
  Features include mission planning, payload verification and drone connectivity .
  Designed for ease of use in Indian markets, improving efficiency and security.
TEAM PHOENIX AERO

## Slide 26
EVENT VIDEOS
(ROUND 1)
TEAM PHOENIX AERO

## Slide 27
TEAM PHOENIX AERO
EVENT VIDEOS (ROUND 2)

## Slide 28
TEAM PHOENIX AERO
THANK YOU